## Slide 1
Final Result
Email signed
AT form to state
Cover Letter
Dual reporting:
eDMR: for test end date,
provide pass or fail result
ATB: Email signed AT Form

## Slide 2
ORC Sign Form
and provide email address
AT Form
Form provides a summary
of the test information
provided on the
laboratory bench sheets

## Slide 3
Ceriodaphnia
Bench Sheets
Control
Test

## Slide 4
Renewal Information
Control Bench Sheet
Date, time and analyst that worked on test

## Slide 5
Ceriodaphnia Chronic Test
Bench Sheet
Control Bench Sheet
Survival recorded and number of offspring counted
each time test solutions are renewed
Test Cup

## Slide 6
Control Organisms Acceptance Criteria
Control Bench Sheet
Organisms < 24-hours old
and born within 8-hour period
Survival and reproduction requirements

## Slide 7
Control Water Acceptance Criteria
Control Bench Sheet
Temperature = 24.0 – 26.0oC
pH = 6.5 – 8.5 S.U.
Hardness = 80 – 100 mg/L CaCO3
≤ 14 days old

## Slide 8
Test Bench Sheet
Effluent Sample
Chemical analyses
Permit specifications
pH = 6.0 – 9.0 S.U.
Dissolved Oxygen
> 5.0 mg/L
Chlorine
< 0.10 mg/L
Statistics: PASS or FAIL

## Slide 9
Program
used to compare survival and reproduction
in the Control
to the Test
Control Bench Sheet
Test Bench Sheet
Statistics

## Slide 10
Statistics
No significant
difference
= “PASS”

## Slide 11
Double Entry and Confirmation
Survival < 67% = FAIL
% Reduction
< 20% = PASS

## Slide 12
Reference Toxicant Testing
Sensitivity of organisms over time
Credibility of testing system
Evaluate testing personnel

## Slide 13
Reference Toxicant Control Chart
Last data point indicates sensitivity of organisms near the time your test was performed